## Slide 1: EL9333 – Lab 6

## Slide 2: Objectives
Learn to develop SDN traffic monitoring applications.
Gain real time traffic measurement experience.
Manage flows in real-time based on traffic measurement

## Slide 3: Major Goals
Monitor traffic in an SDN network
  go through the traffic monitoring example from RYU website: https://osrg.github.io/ryu-book/en/html/traffic_monitor.html
  write a controller to monitor the traffic in a costumed topology in Mininet
Manage flows based on link load
  controller manages the flows among hosts in the costumed topology so that load on each link is evenly distributed

## Slide 4: Traffic Monitoring
Idea: periodically pull port or flow counters on switches for statistics
Two type of counters: port and flow
every 10 secs

## Slide 5: Traffic Monitoring
Port statistics : link load
Flow statistics

## Slide 6: Lab 6 Topology
The following topology the required in lab 6
  a costumed topology file is provided (on NYU Classes)
A costumed command is provided for use in Mininet prompt
  mininet > runTraffic , this will generate udp traffic among hosts
S1
S2
S3
S4
H1
H2
1
2
3
3
2
1
1
2
1
2
S5
H3
3
2
1
3
3

## Slide 7: Lab 6 : Part 1
Write a controller that,
  for new flows, always use the following paths
    H1  H2: S3 – S1 – S4
    H1  H3: S3 – S1 – S5
    H2  H3: S4 – S1 – S5
  monitor the traffic load on each link periodically
    ex: every 5 or 10 secs
    draw a time vs. link load figure for each link
time
traffic load
( x bps: bits/s )

## Slide 8: Lab 6 : Part 2
Write a controller that,
  monitors the traffic load on each link periodically
    ex: every 5 or 10 secs
  based on measured link load, manage the flows so that all links are as evenly loaded as possible
    assign path to new flows based on current traffic load on each link
    re-locate existing flow onto different paths
  draw a time vs. link load figure for each link
    so you can compare with part 1!

## Slide 9: To run the tests
Run Mininet with costumed topology
  sudo mn --custom lab6_topo.py --topo mytopo --mac --switch ovsk --controller remote
Launch your controller code with RYU Manager
  ryu-manager -v your_controller.py
Start the traffic generation among hosts in Mininet prompt
  mininet> runTraffic

## Slide 10: Some hints
ARP is handled
  ARP tables are hard-coded into hosts already
Links are bi-directional
  when pulling port statistics, you have both TX/RX
  background UDP traffic only goes from
    H1  H2, H1  H3 and H2  H3 so you only need to show link load on one direction
Plotting
  you can use python library (ex: matplotlib) to plot the figure within your controller code
  or, you can output the result and use other softwares (ex: Excel)
Traffic measurement,
  run your controller and do the measurement for 10 mins
    traffic generation lasts 10 mins
  all flows are udp, so your rules should specify (IP src, IP dst, src port, dst port, udp)
  flows can join and leave the network at any time